## Slide 1
Validating HOT
Start:
  Start JOSM (with remote control turned on)
  Open in browser: tasks.hotosm.org
  Choose project > “number”
  Read the Instruction, especially “task” and “validation”
  Contribute:
  Choose task to validate (yellow tile)
  > review the work
  > edit with JOSM
  Go to JOSM

## Slide 2
Add imagery: Bing, or other imagery if Bing has clouds
    Adjust offset. In tasks.hotosm.org / instructions > adjust imagery offset” you find the values for X and Y). When you BING imagery no offset required.
    Check correct use of offset. It can happen that for a part of the tile the wrong offset has been used.
  Visual check:
    Total check: if less than 90% is mapped, than continue validating, else disapprove with comment “not finished”.
    Sometimes (often) there are clouds and no other source is available, so a part cannot be mapped. Continue validating for the visual part. Mention this in the comment when you mark the tile as validated.
    If everything or a part is rubbish and correction is more work than a complete new mapping of all objects: delete all or a part of the rubbish. And then invalidate the tile.
    Zoom in and do a visual check on missing objects. Add buildings, roads etc. if necessary, depending on time and importance. Do not expect you map 100%!
    Square buildings. When there a lot of buildings to be squared, you can do it all at once. Go to selection box, select buildings=*. Then square the buildings (shortcut “S”).

## Slide 3
Automatic validation
> Validation. Solve all warnings, except roads without names. With a right mouse click you go to the object.
Usual warnings are:
          Crossing buildings – Unglue the building by selecting node and use shortcut “g”.
          Unnamed ways: leave is, you do not know the name of the road
          Untagged ways: tag it with :highway/residential”
          Untagged building: tag with building/residential
          Crossing ways: put node one right place and merge (shortcut “M”)
          More checks can be done by using the selection box. E.g.: Select: highway=*. Select value “different”. If there are unclassified highways tag them as residential
Do a validation again. If only unnamed ways are left, you finished the validation
4. Upload you changes
5. In the browser put your comment. Pay attention to: clouds, which objecttypes are mapped, changes you did in existing objects
Notes: objecttypes